## Slide 1: Fast Reactor Designing Study for Proliferation Resistance and Physical Protection Enhancement
Pedro Junior Vicente Valdez
SAGARA-Laboratory
Laboratory of Advance Nuclear Energy
Tokyo Institute of Technology Summer Program
Notes: Hi Mi name is Pedro and I will be talking to you about “Fast reactor … enhancement”. This research was undertaken at the SAGARA laboratory in the Laboratory of Advance Nuclear Energy as part of the Tokyo Tech Summer Program.

## Slide 2: Research Plan and Objectives
MCNP4 particle transport code
  Critical mass and heat content calculations
  Neutron transport calculations
  Nuclear material attractiveness methodology
Research on fast spectrum reactor designing for Minor Actinides (MA) transmutation and for High Proliferation Resistance.
Neutronics analysis of a Fast Spectrum Reactor core design:
  Reactivity and burnup calculation by the combination of a 2-D deterministic code, SLAROM-JOINT-CITATION, for full scale fast spectrum core designing and performance evaluation
Learning of the Plutonium (Pu) fuel cycle in Japan. This will include the research of the underlying physics of the Pu fuel cycle.
Notes: As stated in the initial research plan, there were several objectives and goals to be accomplished and they can be resumed in four objectives. First is learning and applying MCNP4 particle transport code for critical mass and heat content calculations, neutron transport calculations and nuclear material attractiveness methodology. Secondly is carrying research on FSR designing for MA transmutation and for high proliferation resistance. Thirdly is the neutronics analysis of a FSR core design. This was done by applying a combination of a 2-D determinist code, SLAROM-JOIN-CITATION for reactivity and burnup calculations. And lastly was to learn about the Pu fuel cycle in Japan including understanding the underlying physics of the Pu fuel cycle. As we will see know all of this objectives were accomplished.
(1:20)

## Slide 3: Important Definitions:
Proliferation Resistance
  is that characteristic of an NES that impedes the diversion or undeclared production of nuclear material or misuse of technology by the Host State seeking to acquire nuclear weapons or other nuclear explosive devices.
Physical Protection
  is that characteristic of an NES that impedes the theft of materials suitable for nuclear explosives or radiation dispersal devices (RDDs) and the sabotage of facilities and transportation by sub-national entities and other non-Host State adversaries.
Notes: First, some important definitions to remember are proliferation resistance and physical protection. Proliferation resistance is that characteristic of an NES that impedes the diversion or undeclared production of nuclear material or misuse of technology by the Host State seeking to acquire nuclear weapons or other nuclear explosive devices. A host state is an actor non-nuclear weapon state assumed to have physical control over the facility and materials being evaluated.
The second definition is Physical Protection which is the characteristic of an NES that impedes the theft of materials suitable for nuclear explosives or radiation dispersal devices (RDDs) and the sabotage of facilities and transportation by sub-national entities and other non-Host State adversaries.
(1)

## Slide 4: MCNP4 – Particle Transport Code
Evaluating Material Attractiveness and Safety of the PUREX process
Notes: The first objective was learning the use of a popular Monte Carlo n-particle transport code. This code can be use for neutron, photon, electron, or coupled neutron/photon/electron transport with applications in radiation shielding protection and dosimetry,, nuclear criticality safety, fission and fusion reactor design, among others.
As stated in the title, using this code, we evaluate the bare critical mass for different elements and isotopes and it’s attractiveness and safety.

## Slide 5: Evaluating Material Attractiveness
Material : bare Pu-Metal, Pu-239, Pu238
Mass density: Pu-metal 15.80g/cc
with delta-phase
Rossi-alpha:
Isotope | radius (cm) | mass (kg) | k-inf | l (abs) | alphaN | decayN | ATTR | ATTR(N)
238 | 5.96 | 14.01 | 2.81324 | 1.27E-08 | 0.96 | 1.00000 | 0.9627619 | 0
239 | 6.22 | 15.93 | 2.95061 | 1.31E-08 | 1.00 | 0.00387 | 258.4596560 | 1
240 | 9.02 | 48.57 | 2.23078 | 4.57E-08 | 0.18 | 0.04316 | 4.1926093 | 0.012543
241 | 6.58 | 18.85 | 2.90547 | 1.23E-08 | 1.04 | 0.00807 | 129.1969948 | 0.498003
242 | 11.3 | 95.50 | 1.9642 | 7.68E-08 | 0.08 | 0.00144 | 58.5002960 | 0.223449
Chart: Attractiveness (Decay Heat)
| 238 | 239 | 240 | 241 | 242
ATTR(N) | 0 | 1 | 0.012543 | 0.498 | 0.22345
Isotope | Decay heat (W/kg) | SN (n/g/s)
238Pu | 567 | 2660
239Pu | 1.93 | 0.0226
240Pu | 7.06 | 1030
241Pu | 3.4 | 0.0493
242Pu | 0.12 | 1720
Notes: For Exercise number 5 we used a methodology to evaluate the attractiveness of different isotopes, in this case Plutonium. ATTR is defined as the ratio of potential explosive yield factor of fissionable materials to characteristics of technical difficulty factor in manufacturing NED. The potential explosive yield factor was defined as a power function of Rossi-alpha (the ratio of supercriticality to prompt neutron lifetime) of infinite mass fissionable materials.
Prompt neutron lifetime is the average time from a prompt neutron emission to either its absorption(fission or radiative capture) or to its escape from the system.
the technical difficulty factor is assumed as the decay heat per unit mass of the fissionable materials (DH [W/kg]) for the application of the new criteria based on decay heat. Decay heat is the heat released as a result of radioactive decay.
Rossi-alpha and decay heat are normalized by the Rossi-alpha of pure 239Pu and the decay heat of 238Pu, which is the maximum value in Pu isotopes. It can be seen from the table that Pu-238 has the highest decay heat while Pu-239 is amongst those with the lowest decay heat factors. From the MCNP output we gather the information needed including mass, k-inf and prompt neutron lifetime. Finally we obtain the normalized attractiveness. It can be seen that this methodology correctly categorizes each isotope by resulting in high attractive for Pu-239 and Pu-241 and low attractiveness of the other isotopes.
(2:10)

## Slide 6
Criticality Safety of Chemical Process in Pulse column
Material : Pu and U in solution
Mass density: Water solution, fix with 1.0g/cc
Pulse Column: Variable Diameter (cm), infinite column
Parameters: Pu density, U-Pu composition
Material Form | radius (cm) | k-eff
Pu(-0.2) | 27.8 | 1.00095
Pu(-1.0) | 13.4 | 0.99959
PuU (0.72/7.2) | 21.44 | 0.99954
PuU (0.36/7.2) | 28.75 | 1.00049
PuU (0.5/8) | 25.18 | 1.00018
Notes: Finally we used MCNP for criticality safety in chemical process in pulse column. To reduce the proliferation risk, the Rokkasho Reprocessing Plant adopted the Plutonium-Uranium Co-extraction Technology that combines recovered uranium with separated plutonium before denitration. Through this process, plutonium is recovered as uranium-plutonium mixed oxide (MOX) at the end of the process, so that the plutonium is never recovered on its own. Therefore criticality safety is important to determine the appropriate radius of the pulse column use in this process to prevent the solution achieving criticality. After running the code I found out that depending on the material form and composition the radius ranges from 13.4 to 28.75 cm. In a real plant this is approximately true (around 20 cm radius). This type of calculations are important to ensure safety in this type of plants especially in Japan, a reprocessing country.
(2)

## Slide 7: SLAROM-JOINT-CITATION
Nuclear Reactor Core Analysis Code
Notes: Proliferation of undeclared nuclear material has been an issue ever since nuclear detonation was proven. Therefore, effective proliferation resistance is required and is then important not only for national but also international security. During the nuclear fuel cycle, measures can be taken beforehand in the reactor design phase to prevent attractiveness of various materials, especially plutonium, for use in nuclear explosive devices (NEDs). As we know, when considering FBR, plutonium becomes a concern. While the discharge fuel on FBR core consists of 60-70% fissile isotopes Pu-239 and Pu-231, the remainders are even mass number plutonium isotopes but contrary to this, in the blanket there are larger amounts of Pu-239 and therefore very small amounts of Pu-239. This means that before widely adopting this type of HBR, this proliferation concerns must be address to ensure proliferation resistance through all the nuclear fuel cycle. In the following research I replicated the material barriers approach to enhance proliferation resistance of the system and more specifically of the blanket. By materials barriers I mean more specifically and isotopic barrier using properties like decay heat and spontaneous fission neutron generation rate.
(5)

## Slide 8: Japan Sodium-cooled Fast Reactor (JSFR)
(Sagara et al., 2005).
Notes: The core concept used was the high breeding 3530 MWth JSFR. The fuel material is mainly TRUO2-UO2 with inner and outer core enrichment of 18.3 and 20.9 wt..% respectively and U-235 enrichment of 0.2 wt..%. The blanket fuel material in the Reference core is purely UO2 also with 0.2 wt.% enrichment. The axial blanket thickness is the same in the upper and lower region, each 20 cm. The image on the right is the fuel rod design. As you can see the axial blanket is in the some structure as the core therefore they are usually process together at discharge.
(2)

## Slide 9: Core design approaches
Nuclide | Composition (wt..%)
238Pu | 1.1
239Pu | 54.1
240Pu | 32.1
241Pu | 4.3
242Pu | 3.9
237Np | 0.5
241Am | 2.0
243Am | 1.0
244Cm | 1.0
(Meiliza et al., 2014)
Notes: Five core design approaches we’re simulated replicating work done by Sagara, Rie and Saito, Meiliza,. The first is the reference core mentioned previously with a UO2 axial and radial blanket. The second design consists on the reference core but without a radial blanket and replaced for a SS. This is immediately resultant in a less proliferation concern due to fact that the core and the axial blanket are usually reprocess together because of the integrated type core fuel pin. The third core was design to utilize the effect of spontaneous fission neutron generation by pu-240 by loading the blanket with plutonium. The fourth design was using the decay heat of Pu-238 by increasing the MA content in the blanket. And the final design was utilizing the combination of spontaneous fission and decay heat by Pu and MA loading into the blanket. This table gives the composition of the fuel used in this simulations.
(1:35)

## Slide 10: SLAROM-JOINT-CITATION
SLAROM-UF
  Cell homogenization calculation
  Fast power reactor
  Fast critical assembly
  Using the Japanese Evaluated Nuclear Data Library (JENDL-3.2)
JOINT-FR
CITATION
  Nuclear reactor core analysis code system
  Neutron diffusion theory
  Two-dimensional RZ diffusion theory
  Depletion Chain
  Multi-cycle analysis
(Naganuma et al., 2005).
Notes: The calculations where done using SLAROM which does cell homogenization calculation in fast power reactor and fast critical assembly's using the JENDL, using JOINT FR and using CITATION a nuclear reactor core analysis code system that solves problems using finite difference representation of neutron diffusion theory and the two dimensional RZ diffusion theory taking into account a depletion chain and capable of providing multi-cycle analysis.
(1)

## Slide 11: Decay Chain
(Meiliza et al., 2008)
Notes: It is important to remember why this scenarios are chosen and why this minor actinides.
There are two pathways for producing 238Pu by MA transmutation. One is through β- decay from 238Np (T1/2 =2.36 d), which is produced from 237Np neutron capture reactions, and the other is through alpha decay from 242Cm (T1/2 = 162.79 d), which is the β- decay daughter of 242Am produced from 241Am neutron capture reactions.
Plutonium-242 is produced through β- decay from 242Am (T1/2 = 16 h), which is produced from 241Am neutron capture reactions, and 240Pu are produced through alpha decay from 244Cm (T1/2 = 18.1 y), which is the β- decay daughter of 244Am produced from 243Am neutron capture reactions.
(1)

## Slide 12: Pu-239 Isotopic Fraction remains high throughout cycle
Chart: Burnup (days)
| 20 | 80 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200
Pu-239 REF | 0 | 0.99972 | 0.99837 | 0.99678 | 0.99525 | 0.99376 | 0.9923 | 0.99088 | 0.98947 | 0.98807 | 0.98669 | 0.98531 | 0.98394 | 0.98257 | 0.98119 | 0.97981 | 0.97842 | 0.97703 | 0.97562 | 0.9742 | 0.97277 | 0.97133 | 0.96987 | 0.9684 | 0.96691 | 0.96541 | 0.96389 | 0.96235 | 0.9608 | 0.95923 | 0.95763 | 0.95602 | 0.95439 | 0.95274
Pu-239 Pu | 0.56649 | 0.56863 | 0.57888 | 0.59065 | 0.60138 | 0.61123 | 0.62032 | 0.62877 | 0.63666 | 0.64406 | 0.65104 | 0.65763 | 0.66387 | 0.66979 | 0.67542 | 0.6808 | 0.68594 | 0.69086 | 0.69557 | 0.70008 | 0.70441 | 0.70856 | 0.71255 | 0.71637 | 0.72004 | 0.72355 | 0.72692 | 0.73015 | 0.73324 | 0.7362 | 0.73904 | 0.74174 | 0.74433 | 0.74679
Pu-239 MA | 0 | 0.80744 | 0.81345 | 0.80304 | 0.7941 | 0.78695 | 0.78125 | 0.7767 | 0.77303 | 0.77008 | 0.76765 | 0.76565 | 0.76398 | 0.76261 | 0.76146 | 0.76051 | 0.75971 | 0.75905 | 0.75849 | 0.75803 | 0.75764 | 0.75732 | 0.75705 | 0.75682 | 0.75664 | 0.75649 | 0.75636 | 0.75625 | 0.75615 | 0.75606 | 0.75599 | 0.75592 | 0.75585 | 0.75578
Pu-239 PuMA | 0.56649 | 0.56926 | 0.58229 | 0.59649 | 0.60882 | 0.61968 | 0.62935 | 0.63807 | 0.64598 | 0.65326 | 0.65996 | 0.66617 | 0.67195 | 0.67735 | 0.68243 | 0.68722 | 0.69173 | 0.696 | 0.70005 | 0.70389 | 0.70754 | 0.71101 | 0.71431 | 0.71745 | 0.72044 | 0.72329 | 0.726 | 0.72859 | 0.73104 | 0.73338 | 0.7356 | 0.73771 | 0.73971 | 0.74161
Notes: No matter which one you use, Pu-239 always high.

## Slide 13: Spontaneous Fission Rate Strategy (Pu-240)
Chart: Pu-240 Spontaneous Fission Rate Strategy
| 20 | 80 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200
Pu-240 REF | 0 | 0.00028181 | 0.0016195 | 0.0031933 | 0.0047085 | 0.0061776 | 0.00761 | 0.0090128 | 0.010392 | 0.011757 | 0.013108 | 0.014449 | 0.015782 | 0.017114 | 0.018446 | 0.01978 | 0.02112 | 0.022464 | 0.023817 | 0.025178 | 0.026548 | 0.027929 | 0.02932 | 0.030724 | 0.03214 | 0.033567 | 0.035008 | 0.036463 | 0.037931 | 0.039415 | 0.040914 | 0.042426 | 0.043954 | 0.045497
Pu-240 Pu | 0.33613 | 0.33453 | 0.32678 | 0.31789 | 0.3098 | 0.30238 | 0.29555 | 0.28921 | 0.2833 | 0.27777 | 0.27257 | 0.26766 | 0.26302 | 0.25863 | 0.25445 | 0.25048 | 0.24668 | 0.24305 | 0.23958 | 0.23626 | 0.23308 | 0.23004 | 0.22712 | 0.22433 | 0.22165 | 0.21909 | 0.21664 | 0.2143 | 0.21207 | 0.20993 | 0.20789 | 0.20595 | 0.2041 | 0.20235
Pu-240 MA | 0 | 0.13188 | 0.11481 | 0.11322 | 0.11315 | 0.11351 | 0.11405 | 0.11466 | 0.11528 | 0.11588 | 0.11645 | 0.117 | 0.11751 | 0.11798 | 0.1184 | 0.11879 | 0.11914 | 0.11945 | 0.11974 | 0.12 | 0.12024 | 0.12046 | 0.12067 | 0.12086 | 0.12105 | 0.12123 | 0.12141 | 0.1216 | 0.12179 | 0.12198 | 0.12218 | 0.12239 | 0.12261 | 0.12284
Pu-240 PuMA | 0.33613 | 0.33396 | 0.32344 | 0.31159 | 0.30104 | 0.29159 | 0.28309 | 0.27538 | 0.26836 | 0.26191 | 0.25596 | 0.25046 | 0.24534 | 0.24058 | 0.23611 | 0.23191 | 0.22796 | 0.22423 | 0.2207 | 0.21737 | 0.2142 | 0.2112 | 0.20836 | 0.20565 | 0.20309 | 0.20065 | 0.19834 | 0.19614 | 0.19406 | 0.19209 | 0.19022 | 0.18846 | 0.18679 | 0.18522

## Slide 14: Decay Heat Isotopic Barrier Strategy (Pu-238)
Chart: Pu-238 Decay Heat Isotopic Barrier
| 20 | 80 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200
Pu-238 REF | 0 | 1.4162e-06 | 7.9391e-06 | 1.5787e-05 | 2.3486e-05 | 3.1089e-05 | 3.8635e-05 | 4.6155e-05 | 5.3674e-05 | 6.1237e-05 | 6.8848e-05 | 7.6523e-05 | 8.4281e-05 | 9.2155e-05 | 0.00010016 | 0.00010831 | 0.00011662 | 0.00012512 | 0.0001338 | 0.00014269 | 0.00015179 | 0.00016112 | 0.00017069 | 0.00018052 | 0.00019061 | 0.00020096 | 0.00021161 | 0.00022256 | 0.00023382 | 0.00024541 | 0.00025734 | 0.00026962 | 0.00028226 | 0.00029528
Pu-238 Pu | 0.011518 | 0.011449 | 0.011149 | 0.010829 | 0.010554 | 0.010314 | 0.010099 | 0.0099036 | 0.009724 | 0.0095571 | 0.0094008 | 0.0092538 | 0.0091151 | 0.0089839 | 0.0088589 | 0.0087399 | 0.0086262 | 0.0085175 | 0.0084137 | 0.0083141 | 0.0082188 | 0.0081276 | 0.0080403 | 0.0079566 | 0.0078765 | 0.0077998 | 0.0077265 | 0.0076564 | 0.0075894 | 0.0075253 | 0.0074641 | 0.0074058 | 0.0073502 | 0.0072973
Pu-238 MA | 0 | 0.037594 | 0.050832 | 0.063265 | 0.072487 | 0.0794 | 0.084627 | 0.08861 | 0.091667 | 0.094016 | 0.09584 | 0.097261 | 0.098368 | 0.099223 | 0.099881 | 0.10038 | 0.10076 | 0.10103 | 0.10122 | 0.10134 | 0.1014 | 0.10142 | 0.10139 | 0.10132 | 0.10122 | 0.1011 | 0.10094 | 0.10077 | 0.10058 | 0.10036 | 0.10013 | 0.099884 | 0.099621 | 0.099343
Pu-238 PuMA | 0.011518 | 0.011562 | 0.012063 | 0.013133 | 0.01444 | 0.015826 | 0.017203 | 0.018527 | 0.019775 | 0.020942 | 0.022027 | 0.023034 | 0.023967 | 0.024832 | 0.025635 | 0.026382 | 0.027077 | 0.027725 | 0.028331 | 0.028897 | 0.029426 | 0.029922 | 0.030387 | 0.030823 | 0.03123 | 0.031613 | 0.03197 | 0.032304 | 0.032617 | 0.032909 | 0.03318 | 0.033433 | 0.033667 | 0.033884

## Slide 15: Initial Reactivity is mostly unchanged
Chart: Multiplication Factor, k-eff
| 20 | 80 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200
k-eff-REF | 1.0471 | 1.0459 | 1.0447 | 1.0432 | 1.0414 | 1.0396 | 1.0375 | 1.0353 | 1.033 | 1.0305 | 1.0279 | 1.0252 | 1.0223 | 1.0194 | 1.0164 | 1.0133 | 1.0102 | 1.007 | 1.0037 | 1.0005 | 0.99717 | 0.99384 | 0.9905 | 0.98713 | 0.98377 | 0.98039 | 0.977 | 0.97361 | 0.9702 | 0.96681 | 0.96343 | 0.96004 | 0.95666 | 0.95328
k-eff-NB | 1.0459 | 1.0447 | 1.0436 | 1.0421 | 1.0403 | 1.0384 | 1.0363 | 1.0341 | 1.0316 | 1.029 | 1.0263 | 1.0234 | 1.0204 | 1.0173 | 1.0142 | 1.0109 | 1.0076 | 1.0042 | 1.0008 | 0.99736 | 0.99386 | 0.99034 | 0.98679 | 0.98321 | 0.97962 | 0.97601 | 0.97239 | 0.96875 | 0.96511 | 0.96146 | 0.9578 | 0.95413 | 0.95046 | 0.94679
k-eff-Pu | 1.054 | 1.0528 | 1.0515 | 1.0499 | 1.0481 | 1.0463 | 1.0443 | 1.0421 | 1.0399 | 1.0375 | 1.035 | 1.0324 | 1.0297 | 1.0269 | 1.024 | 1.0211 | 1.018 | 1.015 | 1.0119 | 1.0087 | 1.0056 | 1.0024 | 0.99913 | 0.99588 | 0.99262 | 0.98935 | 0.98609 | 0.98279 | 0.97949 | 0.9762 | 0.97291 | 0.96963 | 0.96634 | 0.96306
k-eff-MA | 1.0463 | 1.0451 | 1.0439 | 1.0423 | 1.0406 | 1.0387 | 1.0367 | 1.0345 | 1.0321 | 1.0297 | 1.0272 | 1.0245 | 1.0217 | 1.0189 | 1.0159 | 1.0129 | 1.0099 | 1.0068 | 1.0037 | 1.0005 | 0.9973 | 0.99409 | 0.99085 | 0.98759 | 0.98434 | 0.98108 | 0.97782 | 0.97457 | 0.97129 | 0.96803 | 0.96478 | 0.96154 | 0.9583 | 0.95507
k-eff-PuMA | 1.0511 | 1.0499 | 1.0487 | 1.0471 | 1.0453 | 1.0435 | 1.0415 | 1.0394 | 1.037 | 1.0347 | 1.0322 | 1.0296 | 1.0269 | 1.024 | 1.0212 | 1.0182 | 1.0152 | 1.0121 | 1.009 | 1.0059 | 1.0027 | 0.99952 | 0.9963 | 0.99306 | 0.98982 | 0.98656 | 0.98328 | 0.98001 | 0.97674 | 0.97347 | 0.9702 | 0.96693 | 0.96368 | 0.96043
Case | Initial K-eff | Change (%)
REF | 1.0471084 | -
No Blanket | 1.0459388 | 0.11
Pu loading | 1.0539622 | -0.77
MA loading | 1.0463084 | 0.73
PuMA loading | 1.0510942 | -0.46
Case | VRC | Change (%)
REF | 0.00022537 | -
No Blanket | 0.00021632 | -4.02
Pu loading | 0.00023405 | 8.20
MA loading | 0.00022602 | -3.43
PuMA loading | 0.00023156 | 2.45

## Slide 16: Void Reactivity Coefficient
Chart: Reactivity
| 20 | 80 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000 | 3100 | 3200
VRC-REF | 0.00022537 | 0.00022452 | 0.00022019 | 0.00021527 | 0.00021027 | 0.00020563 | 0.00020131 | 0.00019684 | 0.00019374 | 0.00019069 | 0.00018786 | 0.00018482 | 0.00018284 | 0.00018079 | 0.00017913 | 0.00017769 | 0.00017614 | 0.00017517 | 0.00017414 | 0.00017297 | 0.00017216 | 0.00017144 | 0.00017077 | 0.00017018 | 0.00016947 | 0.00016918 | 0.00016873 | 0.00016829 | 0.00016808 | 0.00016774 | 0.00016711 | 0.00016689 | 0.00016669 | 0.00016652
VRC-NB | 0.00021632 | 0.00021541 | 0.00021117 | 0.0002059 | 0.00020064 | 0.00019554 | 0.00019033 | 0.00018603 | 0.00018234 | 0.00017874 | 0.0001747 | 0.00017169 | 0.00016891 | 0.00016639 | 0.00016414 | 0.00016187 | 0.00016016 | 0.00015837 | 0.00015677 | 0.00015529 | 0.0001539 | 0.00015261 | 0.00015135 | 0.00015022 | 0.00014912 | 0.00014808 | 0.0001471 | 0.00014623 | 0.00014524 | 0.00014436 | 0.00014352 | 0.00014275 | 0.00014195 | 0.0001411
VRC-Pu | 0.00023405 | 0.00023339 | 0.00022948 | 0.00022483 | 0.00022022 | 0.00021582 | 0.00021164 | 0.00020719 | 0.00020375 | 0.0002009 | 0.00019809 | 0.00019544 | 0.00019288 | 0.00019065 | 0.00018874 | 0.00018703 | 0.00018558 | 0.00018416 | 0.00018308 | 0.00018202 | 0.00018075 | 0.00017986 | 0.00017903 | 0.00017829 | 0.00017759 | 0.00017695 | 0.00017613 | 0.00017562 | 0.00017549 | 0.00017498 | 0.00017448 | 0.00017367 | 0.00017327 | 0.00017303
VRC-MA | 0.00022602 | 0.00022526 | 0.00022099 | 0.00021611 | 0.00021127 | 0.00020679 | 0.00020265 | 0.00019837 | 0.0001955 | 0.00019262 | 0.00019007 | 0.00018741 | 0.00018557 | 0.00018383 | 0.00018241 | 0.00018113 | 0.00017998 | 0.00017897 | 0.00017825 | 0.00017758 | 0.00017705 | 0.00017652 | 0.00017608 | 0.00017593 | 0.00017533 | 0.00017504 | 0.00017499 | 0.00017452 | 0.00017459 | 0.00017417 | 0.000174 | 0.00017372 | 0.00017366 | 0.00017355
VRC-PuMA | 0.00023156 | 0.00023085 | 0.00022683 | 0.00022209 | 0.00021744 | 0.00021298 | 0.00020863 | 0.00020436 | 0.00020139 | 0.00019833 | 0.00019561 | 0.00019304 | 0.00019031 | 0.00018867 | 0.00018696 | 0.00018528 | 0.00018396 | 0.00018252 | 0.0001817 | 0.00018053 | 0.00017966 | 0.00017889 | 0.00017824 | 0.00017763 | 0.00017731 | 0.00017682 | 0.00017626 | 0.00017583 | 0.00017559 | 0.00017522 | 0.00017484 | 0.00017428 | 0.00017379 | 0.00017345
Case | Mean VRC | Change (%)
REF | 0.00018349 | -
No Blanket | 0.00016701 | -8.98
Pu loading | 0.00019229 | 15.14
MA loading | 0.00018735 | -2.57
PuMA loading | 0.00019091 | 1.90

## Slide 17: Specifications and core characteristics
Item | Unit | HBC | Blanket Free | Pu Loading | Am/Cm Loading | Pu/MA Loading
a) Plant |  |  |  |  |  | 
Axial Blanket Thickness (upper/lower) | cm | 20/20 | 20/20 | 20/20 | 20/20 | 20/20
Breeding Ratio |  | 1.12 | 1.04 | 1.07 | 1.09 | 1.08
Transmutation Rate | % | - | - | - | 17.00 | 16.02
Initial Pu Fissile Inventory | [t/GWe] | 9.395 | 9.395 | 10.446 | 9.392 | 10.095
Pu Reduction Ratio |  | -0.0874 | -0.0393 | -0.0565 | -0.1027 | -0.0720
Discharge Burnup |  |  |  |  |  | 
Core | GWd/t | 139.6 | 87.4 | 83.3 | 84.2 | 83.7
Total | GWd/t | 52.0 | 59.2 | 52.0 | 52.0 | 52.0
Void Reactivity Coefficient |  | 1.83E-04 | 1.67E-04 | 0.00E+00 | 1.87E-04 | 1.91E-04
Blanket TRU enrichment | [wt.%] | - | - | 3 | - | 2
Blanket MA fraction | [wt.%] | - | - | - | 5 | 2
Notes: These are the major specifications and core characteristic obtained. As mentioned previously, all that was changed was the composition therefore leaving the thickness of the blankets unchanged. This was done to analyze the effect of just the composition before changing structural measurements and going into more complex studies.
For the reference core
For the blanket free a breeding ration of 1.04 was obtained,
For the Pu loading case a breeding ratio of 1.07 was obtained but can be increase by modifying the axial blanket and core height (ongoing calculations). There is an increase in pu fissile inventory compare to the REF case.
For the Am/Cm loading case. In this case a breeding ratio of 1.09 was obtained. Modifying core design parameters this can be increase. A transmutation rate of 17% was obtained using 5% MA fraction in the blanket.
In the PuMA case, the last two effects are combined together and a breeding ratio of 1.08 was obtained and a transmutation rate of 16.02% This was done by utilizing a blanket tru enrichment of 2% and blanket MA fraction of 2%
It is important to notice that discharge burnup change which I still dont understand completely.

## Slide 18: Isotopic composition in discharged fuel
Notes: Proliferation resistance measures were the plutonium isotopic fraction. The Categorization done by Kessler (2007) was used stating that more than 9% pu-238 isotopic fraction was sufficient to be regarded as proliferation resistant due to decay heat and radiation. While Mcdonald (2005) stated that at least 18% Pu-240 was also sufficient for proliferation enhancement due to contribution of high spontaneous fission rate.
It can be seen that for the reference core blanket that the UO2 produces high grade plutonium in the range of weapon grade. The discharged fuel while having large quantities of Pu-239 (around 60%) the content of Pu 240 is also high (30%) therefore it can be regarded in the range of MOX-grade plutonium. This blanket compositions raises concerns and the elimination of the radial blanket is a possible solution.
For the next method in the Pu loading case, the blanket can be regarded as reactor-grade plutonium due to the high content of Pu-240. this means that a possible solution is the addition of Pu in the range of 2% to make the blanket proliferation resistance.
In the case of only MA loading the blanket barely meets the proliferation resistance requirements of Pu-238 which means is another option. Similarly for the Pu/MA loading except that the Pu-240 requirement is barely met and not the Pu-238.

## Slide 19: Research Laboratory Visit
Tsuruga, Fukui Prefecture

## Slide 20: Monju Japanese Sodium-Cooled Fast Reactor
Fukui Prefecture
Notes: On August 2 we went on a field trip to the Fukui Prefecture to see the monju JSFR.

## Slide 21: Fast-Spectrum Reactor Characteristics
Sodium Cooled
MOX-fueled
Loop-type
280 MWe and 714 MWt
Breeding ratio of 1.2
Currently undergoing decommissioning process
Notes: Monju is a sodium cooled, MOX-fueled, loop-type reactor with three primary coolant loops, designed to produce 280 MWe from 714 MWt. It has a breeding ratio of approximately 1.2. This trip was incredible as it allow me to see for the first time as a nuclear engineer a real nuclear reactor and also similar to the one I studied during my research at Tokyo Tech.

## Slide 22: Fugen Advanced Thermal Reactor
Fukui Prefecture

## Slide 23: Advanced Thermal Reactor
165 MWe (557 MWt)
Demonstration reactor
Pressure Tube Type Core
Heavy Water Moderator
Boiling Light Water Coolant

## Slide 24: World Politics and Nonproliferation in the Nuclear Age
Notes: During the summer program not only did I undertake research tasks but I also took the world politics and nonproliferation in the nuclear age course. This course help me understand the fundamentals of nuclear nonproliferation and security through the case studies in world politics and the international community from a variety of speakers including the foreign ministry taro KONO. Some of the topics included the Manhattan project, new nuclear proliferation problems and envisioning the elimination of nuclear weapons among others. It is important for us, nuclear engineers, to understand the potential impact of nuclear technology in politics and nonproliferation and the importance of security and physical protection in todays nuclear related technology systems. Not only is it important to widely accept nuclear energy but it cannot be done with the appropriate assurance that it will be safe to use.

## Slide 25: Questions?

## Slide 26: Acknowledgements
Professor Hiroshi SAGARA
Tokyo Tech summer program staff
Laboratory colleagues
Tokyo Institute of Technology
UC Berkeley
Japan Student Services Organization (JASSO)
Notes: I want to thank SAGARA sensei for allowing to come to his laboratory and teaching me such fundamental knowledge and techniques. I would also like to thank the Tokyo tech summer program staff for all their help. My laboratory colleagues were also we’re pivotal to my learning. I am as well grateful to the Tokyo institute of technology and UC Berkeley and JASSO for their support and making it possible for me to come to this beautiful country and not only acquire technical knowledge but also cultural. Thanks to everybody.