## Slide 1: Sensitivity analysis of burnup performance and Pu mass balance by changing core and blanket fuel design of SFR for flexible Pu management options
1Rie Fujioka*, 1Hiroshi Sagara and 1Chi Young Han
1Tokyo Institute of Technology, Tokyo, JAPAN
fujioka.r.ab@m.titech.ac.jp
International Conference on Nuclear Engineering, July 22th – 26th, 2018; London, UK

## Slide 2: Outline
Introduction
Methodologies of numerical neutronics analysis
Fundamental characteristics of the FRs for two Pu management options
FR core design for rapid reduction of separated Pu
Mass balance and non-proliferation features
Conclusions

## Slide 3: Separated Pu concern and countermeasure
Separated Pu concern
Pu management option to alleviate proliferation concern
Separated Pu concern for proliferation
1 Albright D, etc. Civil Plutonium Stocks Worldwide End of 2014. U.S. Institute for Science and International Security; 2015
Proper balance would be strongly desired to reduce the potential nuclear proliferation concerns by states or non-state actors.
Dilution
Separated Pu reduction
Secured storage
Separated Pu conversion to an irradiated form
Pu reduction by nuclear transmutation
Managerial requirement
Physical requirement
Previous study of FR design
This study of FR design
275 t of separated Pu in 2014
Total amount of civil unirradiated Pu in 10 countries1
Notes: In nuclear security and safeguards regulations [4, 5], the irradiation of the separated Pu in a nuclear reactor leads to a downgrade of the categories and potentially to an abatement of nuclear proliferation concerns.

## Slide 4: Objectives
The fundamental characteristics of FRs for two Pu management options are evaluated.
  Rapid conversion of separated Pu to an irradiated form
  Pu reduction by nuclear transmutation
An innovative FR core design is proposed enabling rapid reduction of separated Pu, as well as presenting equivalent operation and safety performance of a typical FR.
Impact of the innovative FR core design is evaluated on mass balance and non-proliferation features.

## Slide 5: Calculation condition for reference FR (REF)
Core model
Japan sodium-cooled fast reactor (JSFR)
High internal conversion type2
Calculation method
Calculation tool：SLAROM-UF, JOINT-FR, CITATION
Cross section library：UFLIB-J4.0
Simplification: Simulating 4 batch burn-up by 1 batch3
Z
Calculation condition2(REF)
Core model1
2 M. Naganuma, et al., JNC-TN9400 2005-051 (2005)
3 H.W. Graves, NUCLEAR FUEL MANAGEMENT, October 1983
Fuel TRU composition
REF
Notes: Demonstration reactor (FR)のことを言う

## Slide 6: FR design for two Pu management options
Constant of heating power in core
1. Fundamental characteristics of FRs for two Pu management options
LE-MOX: Pu low-enriched MOX (5 wt.%)
HE-MOX: Pu high-enriched MOX (IC/OC=45.8/50.0 wt.%)
DU: Depleted Uranium
SS: Stainless Steel
Core model
No fuel in the blanket
HE-MOX in the core
LE-MOX in the blanket
  Rapid conversion of separated Pu to an irradiated form
  Pu reduction by nuclear transmutation
  High Pu loading amount
  High Pu reduction ratio(ΔMPu/MPu,BOC)
Fuel TRU composition of CASE1, 2, 3, 4
Notes: From two Pu management options, this study use two index.

## Slide 7: Result: Pu mass balance features of 5 core designs
Chart: Pu reduction ratio [-]
| -8.7822246004285981E-2 | -5.954629112037476E-2 | 0.12123967610662281 | 0.22681673059204077 | 0.43014521642793901 | -1.9124706004715577E-2
 | 14.0922 | 14.3055 | 14.7321 | 16.2985 | 17.2256 | 16.8455
CASE 1
CASE 2
CASE 3
CASE 5
REF
The highest Pu loading and Pu reduction ratio
A core design with the blanket fuel regions removed and a higher–enriched loading of MOX fuel in core regions
1. Fundamental characteristics of FRs for two Pu management options
Blanket: DU→LE-MOX
Blanket: DU→SS Shielding
Core: standard MOX→HE-MOX
CASE 4

## Slide 8: Result: Technical challenges in CASE 5
1. Fundamental characteristics of FRs for two Pu management options
Initial excess reactivity
Void reactivity
Higher initial excess reactivity than REF
Positive void reactivity
k, k’：Effective multiplication factor without or with void
%void：Void fraction (72.7%)
Fuel assembly cross section
Inner duct
Gap
Void area
Radial peaking factor =Maximum of
Power peaking factor
Higher peaking factor than REF
Average power density in line
Average power density in entire core
Radial peaking factor in REF: 1.27
Radial peaking factor in CASE5: 1.47
5
33%
R

## Slide 9: Core design goal for rapid reduction of separated Pu
2. FR core design for rapid reduction of separated Pu
Core design goal
  Rapid separated Pu conversion to an irradiated form
  Pu reduction by nuclear transmutation
High initial excess reactivity
Positive void reactivity
High peaking factor
Technical challenges
Three approaches
The age impact of MOX fuel
Placement of gas plenum in the axial blanket
Pu enrichment zoning gradually dense in the outer core
FR core for rapid reduction of separated Pu
with equivalent operation and safety performance of REF
CASE 5: core design with removing the blanket fuel regions and loading higher-enriched MOX fuel in core regions
Notes: タイトルにcore designが入るように

## Slide 10
Pro. Low excess reactivity
Con. worse void reactivity
Use of separated Pu stored for a long term
(Reprocessing was started from 1960s) ⇒Increasing burnable poison of 241Am
The effect of long storage fuel specification
4.5% decrease
30%worse
Chart: Burnup [days]
| 0 | 800 | 1600 | 2400 | 3200
ブランケット変更前 | 0.00022365 | 0.00024836 | 0.00026366 | 0.00027299 | 0.00027697
ブランケット変更後 | 0.00016568 | 0.00018244 | 0.0001934 | 0.00019879 | 0.00019998
Improved void reactivity
Worse void reactivity
Replacement of gas plenum from SS shield in axial blanket
⇒Increasing neutron leakage
21%
CASE 3
CASE 3 with Gas plenum in the axial blanket
Result: The age impact of MOX fuel
2)Result: Placement of gas plenum in the axial blanket
2. FR core design for rapid reduction of separated Pu
High initial excess reactivity
241Pu(-,)→ 241Am
Notes: Worldwide, separated Pu has been produced from irradiated fuels by reprocessing since about the 1960s. Therefore, the separated Pu is assumed to be stored on long-term for 50 years after reprocessing and extracted from the irradiated fuels in Capture 3.

## Slide 11: 3) Result: Pu enrichment zoning gradually dense in the outer core
2. FR core design for rapid reduction of separated Pu
Power peaking factor equivalent to REF with high Pu enrichment
Pu enrichment zoning with a gradual increase in density in the outer core
High peaking factor because of high power density in inner core
Z
Axial relative power density
5
Proposed FR
Axial peaking factor
REF: 1.27
Proposed FR: 1.26
R
Radial relative power density
5
Proposed FR
Radial peaking factor
REF: 1.27
Proposed FR: 1.26
Notes: 出力密度が低い炉心外周部のPu富化度をピーキング係数が基本炉心程度の範囲内で増大

## Slide 12: Summary of proposal FR core design for rapid reduction performance
REF
MOX fuel after 5 years from reprocessing
Proposed FR
MOX fuel after 50 years from reprocessing
2. FR core design for rapid reduction of separated Pu
k, k’： Effective multiplication factor without temperature rise or with temperature rise
∆T: Temperature fraction (500K)
Equivalent operation and safety performance of a typical FR
&
initial 17.5 t Pu loading
0.17 Pu reduction ratio
Characteristics of REF and proposed FR
Proposed FR
Notes: 6分50秒

## Slide 13: Comparison of Pu management scenario
3. Mass balance and non-proliferation features
Proposed FR
Standard PWR
MOX powder from in container

## Slide 14: Result: Mass balance and non-proliferation features
3. Mass balance and non-proliferation features
Mass balance feature
Non-proliferation feature
47.9 t separated Pu (equivalent in Japan)
Pu reduction time
The Categories of MOX fuel irradiated in the FR or the LWR were downgraded in 1-step and the same as those of conventional spent nuclear fuel that exists abundantly worldwide.
(Nuclear material attractiveness)
19.5 y
One unit of
FR
N/A
Long storage
86.5 y
One unit of PWR
Shorter by 1/5th

## Slide 15: Conclusions
The fundamental characteristics of FRs for two Pu management options were clarified;
The innovative FR core design was proposed enabling high initial 17.5t Pu loading and 0.17 Pu reduction ratio, as well as presenting equivalent operation and safety performance as typical FR.
MOX fuel (including 47.9t Pu) irradiated in the innovative FR was the downgraded category within 19.5y and the same as those of conventional spent nuclear fuel that exists abundantly worldwide.
A core design with the blanket fuel regions removed and a higher–enriched loading of MOX fuel in core regions caused the highest Pu loading and Pu reduction ratio.

## Slide 16: Thank you for your kind attention

## Slide 17: Evaluation of fundamental characteristics of FRs for Pu loading and Pu reduction

## Slide 18: FR core design for rapid reduction of separated Pu

## Slide 19: Impact of the innovative FR core on mass balance and non-proliferation

## Slide 20: Mass balance and non-proliferation features
2. FR core design for rapid reduction of separated Pu
Mass balance feature
47.9 t separated Pu equivalent in Japan
19.5 y by proposed FR
86.5 y by standard PWR
y by storage
Total accumulated weight of Actinides and FP in the irradiated MOX FA is 40% smaller than PWR.
Pu reduction time
Non-proliferation feature
MOX fuel irradiated in the FR or the LWR was the downgraded category and the same as those of conventional spent nuclear fuel that exists abundantly worldwide.

## Slide 21: 3) Pu enrichment zoning gradually dense in the outer core
2. FR core design for rapid reduction of separated Pu
Pros. Power peaking coeff. Same as Ref. core, Increasing Pu enrichment
Con. Large amount of excess reactivity
Pu enrichment zoning with a gradual increase in density in the outer core
High peaking factor because of high power density in inner core
HE-MOX
HE-MOX
SS Shield
SS Shield
SS Shield
CASE5
Notes: 出力密度が低い炉心外周部のPu富化度をピーキング係数が基本炉心程度の範囲内で増大

## Slide 22: Result of proposal FR for rapid reduction
REF
Reactivity coefficient and controllability is same as Ref. core
&
Amount of Pu loading
14t → 17.2t
k, k’： Effective multiplication factor without temperature rise or with temperature rise
∆T: Temperature fraction (500K)
*
Fuel:
MOX fuel after 5 years from reprocessing
(Core design by JAEA）
LCFR core
Fuel MOX fuel after 50 years from reprocessing
Pu enrichment
[wt.%]
Pu amount in all core [t]
Axial peaking coefficient (BOC)
Radial peaking coefficient (BOC)
Initial excess reactivity (CR can control until 1.07)
Average
Items
Ref. core
LCFR core
Void coefficient (BOC)
*Doppler coefficient (BOC)
2. FR core design for rapid reduction of separated Pu
Notes: 6分50秒

## Slide 23: Chap.2 Pu management scenarios
Separated Pu conversion to SF rapidly
Pu minimization in SF
TRU utilization with high PR HLW minimization
(Without Rokkasyo Reprocessing plant)
Short term scenario
Issue: Separated Pu 47.8t
With MOX reprocessing
Continuation to use nuclear power
Long term scenario
Issue: Large amount of Pu utilization in fuel cycle
With Rokkasyo Reprocessing plant
Without MOX reprocessing
Middle term scenario
Issue: Large amount of Pu in Spent fuel
(Focus on Japan case)
Notes: Fast I decided Pu management scenarios. In Japanese government nuclear policy, they selected TBR multi-recycle finally. But after fukusima accident, All nuclear power plants were stopped and now few NPP were restarted. So Nuclear policy is not clear. So I extracted the possible 3 background situations. Fast……., second……, third……..
From these, I decided 3 targets and scenarios.

## Slide 24: Three Pu management targets
Separated Pu conversion to an irradiated form downgrading its category required from nuclear security and safeguards regulationsｖ
Separated Pu
Pu stock in spent fuel
  Rapid conversion of separated Pu to an irradiated form
Methods of decreasing non-proliferation concern of Pu
Fast spectrum reactors for Pu management
Due to the high performance of neutron economy in fast spectrum reactors, it has technical margins of core designing to respond to the social demands of Pu burning/sustaining flexibly.
  Pu reduction by nuclear transmutation
Notes: どうしてこの３つのPu management targetを選んだのか、これをどうしてFRの炉心で達成しようとするのかをイントロで書きたい
FRの理由
Due to the high performance of neutron economy in fast spectrum reactors, it has technical margins of core designing to respond to the social demands of Pu burning/sustaining flexibly.

## Slide 25: 3) Pu enrichment zoning gradually dense in the outer core
2. FR core design for rapid reduction of separated Pu
Pros. Power peaking coeff. Same as Ref. core, Increasing Pu enrichment
Con. Large amount of excess reactivity
Chart: The number of Axial direction
| 3 | 4 | 5 | 6 | 7 | 8
基本炉心 | 0.67765 | 1.0103 | 1.2421 | 1.259 | 1.0561 | 0.75484
CASE3-1-2富化度増加前 | 0.62603 | 0.96236 | 1.2135 | 1.2616 | 1.0908 | 0.84569
CASE3-1-2富化度増加後 | 0.83358 | 0.83892 | 1.015 | 1.0798 | 1.0122 | 1.2205
Upper
Lower
Power density ratio distribution in the Axial direction (BOC)
Power peaking coeff.
Ref. core
Base core：before fitting enrichment
Base core：after fitting enrichment
Chart: The number of Radial direction
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
基本炉心 | 1.2656 | 1.2698 | 1.253 | 1.2429 | 1.2196 | 1.1631 | 1.1036 | 1.0516 | 0.99586 | 0.96814 | 0.96614 | 1.0542 | 0.9239 | 0.70991 | 0.46771 | 0.34487
CASE3-1-2富化度増加前 | 1.2391 | 1.2359 | 1.2274 | 1.2125 | 1.1902 | 1.1471 | 1.0974 | 1.0499 | 1.0071 | 0.98141 | 0.97396 | 1.0615 | 0.94068 | 0.73007 | 0.50073 | 0.40504
CASE3-1-2富化度増加後 | 0.9363 | 0.94312 | 0.95324 | 0.96505 | 0.97656 | 0.97855 | 0.98401 | 0.99491 | 1.0184 | 1.0612 | 1.0905 | 1.245 | 1.2041 | 1.1433 | 0.82977 | 0.67593
Center
Outer
Power peaking coeff.
Ref. core
Base core：before fitting enrichment
Base core：after fitting enrichment
Power density ratio distribution in the Radial direction (BOC)
Increase Pu enrichment
（Peaking coeff. same as Ref. core)
Low power density
Notes: 出力密度が低い炉心外周部のPu富化度をピーキング係数が基本炉心程度の範囲内で増大

## Slide 26: 7 core design for for two Pu management options
Core model
Constant of heating power in core
Z
HE-MOX: Pu high-enriched MOX
DU: Depleted Uranium SS: Stainless Steel
1 Fundamental characteristics of FRs
No fuel in the blanket
HE-MOX in the core

## Slide 27: Pu mass balance features of 5 core designs
The highest Pu loading and Pu reduction ratio
A core design with the blanket fuel regions removed and a higher–enriched loading of MOX fuel in core regions
1 Fundamental characteristics of FRs

## Slide 28
DU
DU
DU
REF, CASE1
SS Shield
SS Shield
SS Shield
CASE3
HE-MOX
HE-MOX
DU
DU
DU
CASE4
HE-MOX
HE-MOX
SS Shield
SS Shield
SS Shield
CASE5
LE-MOX
LE-MOX
LE-MOX
CASE2
Standard MOX
Standard MOX
Standard MOX
Standard MOX
Standard MOX
Standard MOX
HE-MOX
HE-MOX
SS Shield
SS Shield
SS Shield
Gas plenum
Gas plenum
SS Shield
CASE3 with Gas plenum
Standard MOX
Standard MOX
IC1
OC1
Gas plenum
Gas plenum
SS Shielding
CASE 5
IC2
OC2
IC2
OC3
OC3
OC4
OC4

## Slide 29
Gas plenum
Gas plenum
SS Shielding
28.1wt.%
28.1wt.%
32.1
32.1
36.0
36.0
18.7wt.%
21.4
24.0
DU
DU
DU
18.3
wt.%
20.9
wt.%

## Slide 30: Pu mass balance features of 7 core design
Target1: Rapid separated Pu conversion
Target2:
Pu reduction
High Pu enrichment in core: Good for Rapid Pu conversion to SF and Pu minimization
SS in BL: Good for Pu minimization
Low Pu enrichment in BL: Good for Rapid Pu conversion to SF
1 Fundamental characteristics of FRs

## Slide 31
1) the age impact of MOX fuel
2) Placement of gas plenum in the axial blanket
Pro. Low excess reactivity
Con. worse void coeff.
k, k’：Effective multiplication factor without void or with void %void：Void fraction (72.7%)
Void coefficient
Chart: Burnup [days]
| 0 | 800 | 1600 | 2400 | 3200
ブランケット変更前 | 0.00022365 | 0.00024836 | 0.00026366 | 0.00027299 | 0.00027697
ブランケット変更後 | 0.00016568 | 0.00018244 | 0.0001934 | 0.00019879 | 0.00019998
Improved void coeff.
Fuel assembly cross section
Inner duct
Gap
Void area
Void generated in core and blanket
Issue in ①: High excess reactivity
Use of separated Pu stored for a long term ⇒241Am decrease excess reactivity
Countermeasure
Issue in ②: worse void coeff.
Axial SS shield is replaced to Gas plenum
⇒Increasing neutron leakage
Countermeasure
About 26%
The effect of change fuel specification
 | 241Pu/241Am [wt.%] | Initial excess reactivity keff | Void coeff.* （BOC） [(k’-k)/%void]
MOX fuel after 5 years from reprocessing | 11.5/0.0 | 1.04 | 
MOX fuel after 50 years from reprocessing | 1.0/11.0 | 1.02 | 
 | 241Pu/241Am [wt.%] | Initial excess reactivity keff | Void coeff.* （BOC） [(k’-k)/%void]
MOX fuel after 5 years from reprocessing | 11.5/0.0 | 1.04 | 
MOX fuel after 50 years from reprocessing | 1.0/11.0 | 1.02 | 
2.2% decrease
30%worse
Base core
Base core with using Gas plenum
2 FR core design for rapid reduction of separated Pu

## Slide 32
Security level
Unirradiated direct use material
Irradiated direct use material
Indirect use material
Category I
Category II
Category III
Frequency of inspection
Categorization of nuclear material in Safeguards
Categorization of nuclear material in physical protection
Fresh MOX fuel of FR and LWR
Irradiated MOX fuel of FR and LWR
Fresh MOX powder stored on the ground